## Slide 1: Aircraft Performance Logger
IIB Project – Easter Presentation

## Slide 2: Problem definition
Performance characteristics of airplanes:
  Ground roll
  Distance to clear 15 m = Take off distance required (TODR)
Accurate data for safety, creation of performance charts
Current methods:
  Expensive DGPS, image processing or laser systems
  By-eye by test pilots
Want a cheap module separate from aircraft.
Performance chart example
Ground roll and TODR definitions

## Slide 3: Project Plan
Michaelmas – Proof of concept
Charactise GPS and pressure sensor
Explore ways to make GPS readings more accurate
Decide on method of measuring distance and altitude going forward
Choose method of controlling electronics
Choose data processing method
Lent – Design, Build
Design PCB
Assembly PCB and module
Program microcontroller
Testing
  Static
  Flight
Write up
Easter – Test, Write up

## Slide 4: ‘Cheap’ DGPS
Errors in readings due to multipath, ionosphere, reflection of signals, etc
Corrections usually done on signals themselves
Blue ‘base’ readings, average is true location
Pair each ‘base’ reading to red ‘roaming’ reading
Find orange error vector between base reading and average
Subtract from red roaming to correct it
Latitude
Longitude

## Slide 5: Results: ‘Cheap’ DGPS doesn’t work
‘100m Test’ True distance = 91.44m | Distance Delta (m) | MSE (m2) | σ (m)
Uncorrected | 1.3602 | 0.0632 | 0.2507
Corrected | 1.3602 | 0.2246 | 0.4734

## Slide 6: Results: The Module
Final Module
GPS Module
Pressure Sensor
Microcontroller
SD Card
UART
I2C
SPI
Switch
LED
LED
LED
Block diagram of design

## Slide 7: Results: Calculating TODR
The run data of distance vs height is plotted.
Assuming a linear rate of climb, the line of best fit for the climbing phase is calculated.
This line is extended for the entire run (orange line).
The average height for the runway is plotted and extended for the length of the whole run (green line).

## Slide 8: Results: TODR and Ground Roll
Ground Roll: 101.91m
TODR : 164.58 m
3.2m jump
Handbook value : 195 m

## Slide 9: Results: Effect of propeller wash
=
Propeller speed increased as take-off starts
Increased airspeed through propeller means lower pressure
Causes an apparent jump in height

## Slide 10: Conclusions
‘Cheap’ DGPS not used as no improvement on accuracy
Method of calculating TODR sometimes overestimates take off point
Pressure sensor accuracy less than desired due to
  Oversampling rate
  Propeller wash
  Dynamic effects
Module, with further development, can measure other parameters, such as landing

## Slide 11: Aircraft Performance Logger
IIB Project – Easter Presentation