## Slide 1: Aircraft Data Logger
IIB Project – Michaelmas Presentation

## Slide 2: Can you land here?
London City Airport (LYC): 1,508m
Courchevel-670 (CVF) : 537m
At altitude
Mountains
18% gradient
Barra Airport (BRR): 680,799,846m
Sand
Tide

## Slide 3: Take-off and landing parameters
Paraments we need:
  Ground Roll – Distance to take off/land
  Distance to clear 50ft (15.2m) – Get over obstacles, ensure great enough climb rate
Depend on:
  Pressure
  Temperature
  Weight
  Windspeed
  Runway surface etc etc
Determine from Performance charts or tables:
  Given conditions, how far do I need?

## Slide 4: Method 1: Calculation
Advantages
Simple, cheap
Can be implemented in software
Method
Take all your parameters, conditions and equations of motion and crunch through it
Drawbacks
Laborious, time consuming
Model gets more complex the more parameters there are

## Slide 5: Method 2: “By-eye”
Method
Plane has all the instruments, runways have distance markings, just judge it while you take off
Drawbacks
Not very accurate
Another thing for the test pilot to be worrying about
Advantages
The simplest bar far
No special equipment or complex calculation required

## Slide 6: Method 3: Differential GPS
Method
Using a GPS base station that has a known, fixed location, correct the errors from the aircrafts GPS to get a accurate reading of distance. Use the altimeter to get distance to clear 50ft.
Drawbacks
DGPS-capable modules are very expensive
Advantages
Most accurate method
Many airports already have base stations

## Slide 7: Goal of Project
Goal “Create a cheap module that can measure accurately ground roll, distance to clear 50ft and distance to descend 50ft for aircraft”
Requirements:
~10Hz data acquisition rate
Get altitude to within 1ft (30cm)
Get distance to within 3ft (1m)
Cheap, small, easy to use module
Post-processing saved data allowed, but real time results desirable

## Slide 8: Plan
Michaelmas – Proof of concept
Characters GPS and pressure sensor
Explore ways to make GPS readings more accurate
Decide on method of measuring distance and altitude going forward
Choose method of controlling electronics
Choose data processing method
Lent – Design, Build, Test
Design PCB
Assembly PCB and module
Program microcontroller
Test module (department aircraft)
Further improvements
  Screen
  Telemetry
Report
Easter – Wrap up

## Slide 9: Current Progress: Cheap DGPS
‘100m Test’ True distance = 91.44m | Distance Delta (m) | MSE (m2) | σ (m)
Uncorrected | 1.3602 | 0.0632 | 0.2507
Corrected | 1.3602 | 0.2246 | 0.4734

## Slide 10: Current Progress: Cheap DGPS
‘50m Test’ True distance = 45.72m | Distance Delta (m) | MSE (m2) | σ (m)
Uncorrected | 2.8443 | 0.5862 | 0.7652
Corrected | 4.3862 | 0.7576 | 0.8703

## Slide 11: Current Progress: Cheap DGPS
Latitude-Longitude plot for the 50m test
Average Location
Variation
‘Uncorrected’
‘Corrected’ ≈ΣErrors

## Slide 12: Current Progress: Altitude
Steady vs Temp
Walk about
Chart: Time (milliseconds)
Chart: Index

## Slide 13: Take aways
DGPS may not be the way to go
  No drastic improvement
  Sometimes makes it worse
Pressure sensor suitable for the roll
Investigate fix vs frequency
Look at a moving roaming station
Does satellites in view have an effect?
Further Work
Corrected
Uncorrected

## Slide 14: Aircraft Data Logger
IIB Project – Michaelmas Presentation